## Slide 1: Control Systems
Sajeeth Kumar
Lecture 05 – Control System Design Part 1
Crank Shaft Position Sensor

## Slide 2: Scope
Engine Control Systems
Crankshaft Speed Resolution
Engine State Recognition
Phase Recognition

## Slide 3: SI Engine Control System

## Slide 4: Crankshaft Speed Resolution
Engine RPM
Naming Nomenclature Total – Missing
Eg 36 – 1
RPM resolution
TDC resolution – Soft TDC
Need for Phase recognition
Other use cases

## Slide 5: Crankshaft Speed Resolution
Engine RPM
Engine is running 36-1 configuration, 14 teeth between TDC and sync tooth
Calculate the soft TDC angle
Calculate the frequency of pulses at 3000 rpm

## Slide 6: Crankshaft Speed Resolution
Engine RPM – Advanced Algorithms
How is Engine RPM related to Vehicle Speed?
Engine is rotating at 4000 rpm in 3rd gear, 3rd gear ratio is 1.3, final drive ratio is 3.2
Calculate the wheel speed
If the wheel size is 205/60/R16, calculate the vehicle speed
What is happening, if the wheel speed suddenly increases?
What is the maximum engine RPM allowed?

## Slide 7: Crankshaft Speed Resolution
Max Engine RPM – Mean Piston Speed
How is maximum engine rpm calculated?
Stress acting on the piston assembly – Tensile and Compressive
Mean piston speed = 2* RPS * Stroke
Limiting factor of max engine rpm
Usual values
  Low Speed Diesel – 8.5 m/s
  Normal Diesel Engines – 11 m/s
  Regular Petrol Engines – 18 m/s
  Sports Cars – 25 m/s

## Slide 8: Engine Phase Recognition
Engine Phase – Stroke in Progress
Essential to identify the exact stroke
Fuel injection – Before suction stroke
Diesel Engines – Pilot, Main and Post injections
Recognized by speed variations
Engine RPM measure at
  90 BTDC – Average of 4-10 Teeth Speeds
  90 ATDC – Average of 4-10 Teeth Speeds

## Slide 9: Engine Phase Recognition
Engine Phase – Stroke in Progress

## Slide 10: Engine Phase Recognition
Engine Phase – Exceptions
While cranking – Interaction between starter motor and flywheel might disrupt readings
Misfire – Reduction in engine speed during power stroke
Encoder error
ECU runs in sequential mode only when conditions are normal
Runs in non-sequential mode otherwise
Capable of forced non-sequential mode by external triggers

## Slide 11: Engine State Resolution
Engine State
Refers to the operating condition of the engine
Primary states are
  Stall
  Cranking
  Running
  Over-Run

## Slide 12: Engine State Resolution
Engine State

## Slide 13: Engine State Resolution
Engine State
How does the engine enter ORC from Stall?
Why do we need to capture engine states?
Who defines the engine states?
Steady state and transients

## Slide 14: Engine State Resolution
Engine State
Engine State | Engine RPM | Throttle Position
Stall | Zero | NA
Cranking | 0 < RPM < Crank Threshold | TPS <= Flood Clear
Flood Clear | 0 < RPM < Crank Threshold | TPS > Flood Clear
Run – Closed Loop | Idle Limit < RPM < Max RPM | TPS < Closed Loop Limit
Run – Open Loop | Idle Limit < RPM < Max RPM | TPS > Closed Loop Limit
Idle | Crank Threshold < RPM < Idle Limit | TPS = 0
WOT | Idle Limit < RPM < Max RPM | WOT Limit < RPM
ORC | ORC Limit < RPM < Max RPM | TPS = 0

## Slide 15: Engine State Resolution
Engine State – Closed Loop Operation
To meet emissions targets – Engine runs in closed loop mode
Closed Loop enabled only when
  Throttle position less than threshold
  Coolant temperature inside limits
  No errors in O2 sensor or related circuits
Control System targets fueling to achieve a stoichiometric mixture
PID control on injector pulse width

## Slide 16: Engine State Resolution
Engine State – Closed Loop Operation
Variations in measured AFR – Changes in throttle & load
PID control / calibration determines effectiveness
Essential to maintain slightly richer than stoichiometric to ensure TWC operation
PID calibration – Limitations
Hence narrow operating window
Closed loop operates on spark advance as well – but LUT based
Injection PWM is commanded, based on RPM and Load, LUT supplies base advance
Advance varied within limits to achieve target AFR

## Slide 17: Thank You!
In our next session:
Plant Model Development