## Slide 1: Control Systems
Sajeeth Kumar
Lecture 06 – Control System Design Part 2
Air & Fuel Requirements

## Slide 2: Scope
Engine Control Systems
Air Mass Calculation – Measured vs Predicted
Fuel Mass Calculation

## Slide 3: SI Engine Control System
Air & Fuel Requirements

## Slide 4: Air Mass Calculation
Measured vs Predicted
Air mass measurement not very accurate – Transient conditions
Measured vs Predicted – Usual cases converges within limits
Measured – Use MAP / MAF sensor
Predicted – Use TPS sensor
Predicted values used for fail safe scenarios as well

## Slide 5: Air Mass Calculation
Air Mass from MAP sensor
P – Pressure of air inside the cylinder - reading from MAP sensor in Pa
V – Volume of air inside the cylinder in m3
R – Gas constant – 287 J/KgK
T – Temperature of air inside the cylinder – reading from Intake Air Temperature Sensor in K
m – Mass of Air in Kg / Stroke

## Slide 6: Air Mass Calculation
Air Mass from MAP sensor
P – Pressure of air inside the cylinder - reading from MAP sensor in Pa
V – Volume of air inside the cylinder in m3
R – Gas constant – 287 J/KgK
T – Temperature of air inside the cylinder – reading from Intake Air Temperature Sensor in K
m – Mass of Air in Kg / Stroke

## Slide 7: Air Mass Calculation
Air Inlet Temperature Model
Temperature of air is an important factor in accurately measuring air mass
Air Temp dependent on
  Temp of air at inlet
  Heat soak
  Engine temperature
IAT sensor alone will not suffice
Temperature compensation model is built – DOE & Testing
Air temperature is offset based on values from LUT
Compensate for air temperature increase due to other factors

## Slide 8: Air Mass Calculation
Air Mass from MAF sensor
MAF sensor calibrated to read air mass in g/s
Total air mass flowing into engine measure directly
Required in cases where engine VE is high – Example?
Forced induction setups – ready around 200-250 kPa ( positive pressures )
MAP sensor is less accurate and slow
MAF reading immediate – BUT
MAF measured just behind air filter
MAP measured in manifold
Variations between MAP and MAF denote leak in intake
MAP sensor on Intercoolers – Charge Pressure Sensor / Boost Pressure Sensor

## Slide 9: Air Mass Calculation
Air Mass Predictions
TPS vs RPM -> VE map -> Theoretical Air Mass in cylinder
Atmos Pr vs TPS -> Vol Correction
Air Temp vs TPS -> Temp Correction
Predicted Air Mass = ( Th Air Mass + Vol Correction ) * Temp Correction * Density / Atmos Pressure
Predicted air flow can be used when sensor failures occur
Fail safe scenarios for multiple sensor failures
Trade-Off between Predicted and Measured air mass for consideration

## Slide 10: Air Mass Calculation
Air Mass Predictions
TPS vs RPM -> VE map -> Theoretical Air Mass in cylinder
Atmos Pr vs TPS -> Vol Correction
Air Temp vs TPS -> Temp Correction
Predicted Air Mass = ( Th Air Mass + Vol Correction ) * Temp Correction * Density / Atmos Pressure
Predicted air flow can be used when sensor failures occur
Fail safe scenarios for multiple sensor failures

## Slide 11: Fuel Mass Calculation
Fuel Mass Predictions
Once Air Mass is resolved -> Fuel Mass Calculation
Base Fuel predictions – closed loop or open loop
Closed Loop – Target AFR
Open Loop – LUT, applicable load factor
Corrections to base fuel – Steady state or transients
Steady State – Warm-Up Enrichment – Summative
Warm Up Offset – Summative

## Slide 12: Fuel Mass Calculation
Fuel Mass Predictions
Other Corrections
  Closed Loop Correction
  Fuel Trims – STFT & LTFT
  Flaring Correction
  Medium Transients
  Wall Wetting
Fast Transient – Corrections?
Applied as a correction factor – Total Fuel Corrections

## Slide 13: Thank You!
In our next session:
Correction factors for Transients