## Slide 1: Control Systems
Sajeeth Kumar
Lecture 07 – Control System Design Part 3
Spark & Other Strategies

## Slide 2: Scope
Engine Control Systems
Calculation of Spark Advance
Hardware Diagnosis
Idle Speed Control

## Slide 3: Spark Advance Calculation
Angle vs mS
Advance calculated based on soft TDC count down
Parameters to be resolved
  Base Spark Advance
  Dwell Time compensation
Spark Advance Map
Dwell Time map
Spark Advance Map – Only for RUN
Separate Advances for “Stall” & “Idle”
Stall – From Cranking requirements
Idle – Closed loop control
Spark advance & retard based on
  IAT
  ECT
  Knock Control
  Failure Scenarios

## Slide 4: Spark Advance Calculation
Spark Mode
Wasted Spark setup
Sequential setup
Failure mode scenarios
Ignition diagnosis

## Slide 5: Hardware Diagnosis
Hardware
Ignition / Injection Drivers
Injectors & Coil Packs
Sensors
Actuators
Gauges
Pump & Fan

## Slide 6: Hardware Diagnosis
Errors & Faults
Errors – A value is out of range
Fault – Unacceptable number of consecutive errors
Raw Value – Sensor value
Filter – Clear noises
All analog inputs
  Calibratable number of errors to cause a fault
  Calibratable default value to revert to, when in fault
  When fault clears, value is changed from “Default” to “Measured”

## Slide 7: Hardware Diagnosis
Errors & Faults
Ignition driver diagnosis
Depending on system, current is measured – 6A in this case
If all is normal, a feed back signal is sent
If time T1 is very less – Short Circuit
If time T1 is more or no feedback is received – Open Circuit
Diagnosis performed only during Stall and Cranking
Voltage threshold to prevent inconsistencies due to low voltage
Kickstarting vs Cranking

## Slide 8: Hardware Diagnosis
Errors & Faults
Ignition driver diagnosis
Depending on system, current is measured – 6A in this case
If all is normal, a feed back signal is sent
If time T1 is very less – Short Circuit
If time T1 is more or no feedback is received – Open Circuit
Diagnosis performed only during Stall and Cranking
Voltage threshold to prevent inconsistencies due to low voltage
Kickstarting vs Cranking

## Slide 9: Hardware Diagnosis
Errors & Faults
Other actuators
  Short to ground
  Short to positive
  Open circuit
  Samples drive signals
  Open circuits – Needs 2x the signal pulsewidths
Diagnosis continuously run – Raises error flags
Fuel injector diagnosed during stall and crank
IAC only during idle
Sensors – Values checked for range as well

## Slide 10: Idle Speed Control
IAC
Closed loop control using solenoid or valve
Required for smooth running of engine
Warm-up conditions – needs more air
Static loads – More air
Simple On-Off control – PWM determines amount of air
On during STALL
Mapped values during CRANK
Can control engine braking – Throttle closed in ORC
Higher air flow – Reduces Engine Braking
Primary function is to ensure idle speed meets set point

## Slide 11: Idle Speed Control
IAC
Idle Ramp – How quick the set point rpm is achieved
Idle stability control – how much the RPM varies from set-point eg 680 +- 50 rpm
Valve open time – Synchronize with valve timing
Delay between electric signal and operation

## Slide 12: Thank You!
In our next session:
Diesel Control Strategies